Lake Thunderbird

5 YEAR

Management Plan

Central Region

FISHERIES DIVISION

oklahoma deptment of

wildlife conservation

prepared by: Keith thomas

September 15, 2008

Introduction:

The purpose of this document is to assemble all pertinent biological and physical data to devise and implement a management plan for improving Lake Thunderbird’s aquatic resources.  To create a more comprehensive plan, all lake stakeholders will be invited to participate in the planning  process.  Plans from other agencies and municipalities that have already been developed and are being implemented will be taken into consideration.

Use and ownership

Lake Thunderbird was constructed by the United States Department of the Interior’s Bureau of Reclamation (BOR) to provide flood control, municipal water supply, recreation and wildlife habitat.    Water usage is governed by the Central Oklahoma Master Conservancy District (COMCD).  The cities of Norman, Del City, Moore and Midwest City rely heavily on Thunderbird for their water supply.  Recreational facilities are managed by the Oklahoma Tourism and Recreation Department (Lake Thunderbird State Park) and the lake ranks high among BOR projects for visitation..

Physical features

Lake Thunderbird is a 6,070 acre reservoir that was constructed in 1965.  It impounds the Little River and Hog Creek at their juncture in Northeast Cleveland County.  The reservoir is located 13 miles east of Norman, Oklahoma at Longitude: 97° 13' 5" and Latitude: 35° 13' 15".

The lake has 86 miles of shoreline which is comprised of clay, sand and sandstone. The shoreline development index is 7.9.  The watershed occupies 256 square miles of residential, commercial and agricultural lands.   The surrounding woodland habitat is comprised of Post and Blackjack oak in the Cross timbers ecotype region of the Southern Plains.  Average annual precipitation is 35.98 inches.

The conservation pool is 1,039 MSL (Mean sea level) and the reservoir has a total capacity of 119,600 acre-feet of water.  The maximum depth near the dam is 57.6 feet and the average depth is 19.70 feet.  The water exchange rate is 1.9 (inflow/storage capacity).

Prevailing winds are out of the SSE most of the year at 5 to 20 mph.   The reservoir receives a total of 3,295 heating degree days.   The lake level fluctuates on average 5.45 ft. each year.   Currently, there is no water level management plan in place to benefit fisheries or wildlife.

Limnological properties

Chemical properties measured by the Oklahoma Water Resources Board (OWRB) in 2004 were within acceptable levels relative to the Oklahoma Water Quality Standards (OWQS).  Normal surface temperatures range from 45 to 85 ºF annually.  The reservoir is somewhat turbid due to colloidal and planktonic particulates throughout the year with a secchi disk reading of 36 inches mid lake.  Samples collected in 2004 indicated turbidity of 24 NTU (nephalometric turbidity units) which is just below the acceptable level described by OWQS.  Salinity values range from 0.16 to 0.23 ppt (parts per thousand).   The water is slightly hard with a reading of 8.2 pH.   The conductivity was 308 to 461 µS/cm.   Dissolved oxygen (DO) readings are above 4 ppm (parts per million) from the surface down to 21 feet during the majority of the year.  The lake stratifies normally in mid-June and forms a thermocline at around 24 feet.  The hypolimnion typically has less than 2.0 ppm DO.  This has caused few problems historically to fish populations with the exception of occasional summer kills of larger saugeye.   The OWRB has identified Lake Thunderbird as being eutrophic. The Carson’s Trophic State Index indicates high primary productivity (TSI = 58).

Habitat types

Some of the major habitat types beneficial to fish and other aquatic organisms include: standing timber (3 %), aquatic vegetation (20%), terrestrial vegetation (10%), rip-rap (10%) and dock structures (2%).  From 1970 to 1990, large beds of Eurasian Watermilfoil (Myriophyllum spicatum) covered the lake.  Partial die offs took place in the mid 1980’s.  A large die off occurred in 1995 (J. Boxrucker, personal communication).  Eurasian Watermilfoil is present today but in small quantities.

Several native aquatic plants species have been introduced by the ODWC and the OWRB in order to increase fish habitat, reduce shoreline erosion and improve water quality.  Beginning in 2000, several sites around the lake were planted and protected with PVC coated welded wire and poultry fencing.   Fencing was installed to exclude herbivores.  Flood and drought conditions have hindered the overall success, but the plants have persisted and introductions continue.

Fish species

Sportfish in Lake Thunderbird include: largemouth bass (Micropterus salmoides), white and black crappie (Pomoxis spp.), blue catfish (Ictalurus furcatus), channel catfish (I. punctatus), flathead catfish (Plyodictus olivaris), white bass (Morone chrysops), saugeye (Sander vitreus x S. Canadensis), bluegill sunfish, green sunfish and redear sunfish (Lepomis spp.).  Bass, crappie and catfish have been the predominant species supporting the fishery.  White bass numbers have fluctuated over the decades.  The saugeye population is supported by annual stockings.

Other endemic fish species include: common carp (Cyprinus carpio), small mouth buffalo (Ictiobus bubalus), big mouth buffalo (Ictiobus cyprinellus), river carp sucker (Carpiodes carpio), fresh water drum (Aplodinotus grunniens), spotted gar (Lepisosteus oculatus), gizzard shad (Dorosoma cepedianum), inland silverside (Menidia beryllina), warmouth and longear sunfish (Lepomis spp.), yellow bullhead (Ameiurus natalis), red shiner (Cyprinella lutrensis), blunt nose minnow (Pimephales notatus) and mosquito fish (Gambusia affinis).

Largemouth bass -

Lake Thunderbird has historically had a low density largemouth bass population.  Possible factors include: lack off adequate nursery habitat, lack of adequate ambush habitat for adult fish, high competition with other sunfish species, low productivity due to turbid conditions and overharvest.  Table 2 reveals that electrofishing catch rates for largemouth bass have been below minimum statewide levels for balanced populations.  However, it has continued to produce fair to good numbers of quality sized fish throughout the years.

A 14-inch minimum length limit was applied in 1989.  The regulation is still in affect today. Angling pressure and harvest have remained stable throughout the years (Figure 6).  Floods and droughts have effected bass reproduction and recruitment.  Figure 2 shows how bass recruitment responded to high and low water levels.  Acceptable numbers of young-of-year fish were sampled in 1990, 1991, 2002 and 2005.

Largemouth bass virus (LMBV) was confirmed in the largemouth bass population from 2000 to 2002.  Isolated fish kills were noticed during the summer months but no large die offs were observed.  According to ODWC bass tournament report data, anglers had to fish longer in order to catch bass over five pounds as a result of the infection (Table 6).  The bass population has recovered according to recent surveys.

Florida largemouth bass were introduced into Lake Thunderbird beginning in 1973 to increase trophy bass numbers.  In some years, fingerlings were reared at the Lake Thunderbird nursery pond (Table 1).

Forage abundance has been adequate to maintain bass body condition with relative weight values near or above 100 (Table 2).

Crappie spp. -

White crappie were historically slow growing or stunted (Boxrucker, 1992). Age and growth studies revealed that fish at or below 6 inches were not converting over to a fish diet until age 6 (Figure 10). Several management tools were applied to correct this situation.  The saugeye, a predator was introduced in 1985.  Trials in Ohio with stunted panfish populations showed positive results when saugeye were introduced.  Additional prey species (inland silversides and threadfin shad, D. pentenense) were stocked as added food for largemouth bass, crappie and saugeye (Table 1).  Crappie size structure has improved in recent years (Figure 15).  Recent trapnet surveys along with reports by anglers have shown a two-fold increase in 10-inch fish compared to previous years (Figure 3).  White crappie condition has remained fair with a mean Relative Weight of 86.0 (Table 3).   Black crappie are present but found in very low numbers.

Saugeye –

Walleye were introduced into Lake Thunderbird as an added sportfish and to help control stunted crappie from 1966 through 1976.  Survival of walleye fry was limited due to predation, low stocking rates, limited food availability, turbidity and less than optimal temperatures.  Saugeye, the walleye x sauger hybrid, was stocked experimentally in 1985 and has been stocked regularly since then (Table 1).  Saugeye fingerlings have been obtained from out-of-state sources, ODWC hatcheries and have been reared at the Lake Thunderbird Nursery pond on occasion.

Saugeye numbers have remained fairly constant in recent years (Table 4).   Electrofishing catch rates have been good compared to statewide averages.  An 18-inch length limit was applied in 1993.  Since then, catches of 10 fish per hour or better have been observed (Figure 4).  Saugeye are in good condition when compared to statewide values with a Relative Weight of 98.4 (Table 4).

Flathead catfish -

Numbers of catfish collected by electrofishing are considered acceptable (Table 5).  A 20-inch minimum length limit was applied to flathead catfish in 1995.

Prey species -

Bluegill, redear, green, longear, and warmouth sunfish numbers are high, Inland silversides numbers are moderate, Threadfin shad abundance is low, Gizzard shad numbers are moderate. Predator Relative Weights and abundance forage abundance information indicate that the system may be at carrying capacity.

Threats to the fishery:

Pollution and trash, OWRB

- Non-point source - storm drain runoff from urban sites and rural seepage

- Point source - None

- Park visitors - discarded trash into the lake

Declining water quality, OWRB

        - Due to erosion and turbidity the lake has average water clarity. The OWRB posted a 24 NTU in 2004.  Listed as partially supporting beneficial use.

        - High algal levels due to high primary productivity according to OWRB.  High phosphorus and nitrogen levels

        - Poor oxygen levels mid Summer and Fall at hypolimnion

Competing Water uses

        - COMCD supplies water from Lake Thunderbird to area municipalities. Currently they supply water to approximately 175,000 persons. The number served will rise to approx. 225,000 by 2010. The capacity of Lake Thunderbird to deliver sufficient water will be met in a few years (COMCD, 2004).

Non-native species

        - Spotted bass (M. punctulatus), grass carp (Ctenopharyngodon idella) , white perch (Morone americana), zebra mussels (Dreissena polymorpha), Quagga mussel (Dreissena rostiformis bugensis), hydrilla (Hydrilla verticillata), salt cedar (Tamarix aphylla) and common reed (Phragmites australis).  All of these are exotic and could be problematic to Lake Thunderbird.  These organisms will compete with native species, destroy native habitat and disrupt the overall balance of the ecosystem.

        - Other water born organisms - Viral hemorrhagic septicemia (VHS) and golden algae (Prymnesium parvum)

        - Fish consumption advisory - The Oklahoma Department of Environmental Quality (DEQ) sampled the lake in 1999 as part of their Toxics Monitoring Program.  There is a statewide advisory for mercury.  Children under age 15 and women of childbearing age are advised to consume no more than one meal per week of predator species. No other compounds were detected at the DEQ screening or consumption advisory level. The lake is fully supporting its Fish Consumption beneficial use.

Review and include existing plans from other agencies:

        - OWRB - Beneficial Use Monitoring Plan (BUMP)

        - ODWC - Conservation Wildlife Management Strategy (CWMS) and HACCP (Hazard Analysis and Critical Control Point) plans

        - City of Norman Storm Water Plan

        - Watershed development and land use practices (shoreline erosion and siltation) follow OWRB and Oklahoma Conservation Commission plans (Project 10)

        - Oklahoma Comprehensive Water Plan

Management Objectives:

Regulations

- Initiate age and growth study on largemouth bass using FAST model (Spring 2008) and evaluate current 14-inch largemouth bass length limit

- Evaluate current 18-inch saugeye length limit using FAST model

- Increase all LMB, WC, SGE and BC Wr and CPUE in 5 years by 5 %

Sampling schedule

- Trap netting for crappie - monitor catch, size structure, age & growth and trends (3 yr cycle starting in 2009)

- Electrofishing for bass - catch (annual assessment), age & growth, size structure and trends (3 year cycle starting in 2008)

- Electrofishing for catfish - catch, age & growth, size structure and trends (3 year cycle starting in 2009)

- Gill netting for shad - catch, size structure and trends (2 year cycle starting in 2008)

- Gill netting for white bass - catch, size structure and trends (3 yr cycle start in 2009)

Fish stocking

- Renovate Lake Thunderbird nursery pond and produce advanced FLMB fingerlings in 2009.

- Continue stocking saugeye fingerlings at 20/acre following ODWC Stocking Criteria.

- Stock threadfin shad in 2009 to provide additional prey for saugeye, crappie and bass.

- Rotate species at nursery pond 1st year with bass, 2nd year with saugeye and 3rd year with channel catfish.  Catfish will be raised for AREP events and lake stockings.

Habitat improvement projects

- Negotiate with COMCD and BOR to maintain stable lake level during spring and summer months in order to improve bass and sunfish recruitment.

- Continue aquatic plant introductions by maintaining existing sites and adding new locations with appropriate permission and compliance documents.

- Continue brush pile construction and maintenance.

- Construct additional gravel shoals on road beds and points with 2-inch coarse gravel or larger stone.  Evaluate effectiveness of sites with electrofishing surveys.

- Mark all habitat sites with fish attractor buoys, maintain existing buoys, record and publish GPS coordinates.

Angler satisfaction

- Conduct creel survey on Lake Thunderbird every 3 years (start in 2010)

- Utilize Sportfish Restoration Boating and Fishing access funds to improve existing sites and add new ones.  Coordinate with State Parks, Absentee-Shawnee Tribe, BOR and Friends of Lake Thunderbird.

- Conduct annual stakeholder meetings to exchange information on management progress and get input on modifications that the public would like to see.

References

Boxrucker, Jeff.  1992.  Growth responses of white crappie and recruitment of largemouth bass following the introduction of threadfin shad in Thunderbird Reservoir.  Oklahoma Department of Wildlife Conservation, Federal Aid Report Final Report. F-37-R-15 Job 15. Oklahoma City. 27pp.

Oklahoma Water Resources Board. 2004.  Lake Thunderbird Capacity and Water Quality 2004.  Report to the Central Oklahoma Master Conservancy District. Oklahoma City. 12 pp.

Contact Information

Bureau of Reclamation Area Office (Oklahoma-Texas)
5316 Highway 290 West, Suite 510
Austin, TX 78735-8931

Internet: www.usbr.gov

Phone: (512) 899-4150
Fax: (512) 899-4179

Bureau of Reclamation - Oklahoma City Field Office
5924 NW 2nd Street Suite 200
Oklahoma City, OK 73127

Phone: (405) 470-4800
Fax: (405) 470-4807

Oklahoma Water Resources Board

3800 N. Classen Blvd. 
Oklahoma City, OK 73118

Internet: www.owrb.ok.gov

(405)530-8800
(405)530-8900 FAX

Okla. Department of Environmental Quality
707 N Robinson 
Oklahoma City, OK 73102

Internet: www.deq.state.ok.us

405-702-1000
Fax: 405-702-1001

Lake Thunderbird State Park
13101 Alameda Dr
Norman, OK 73026

Internet: www.touroklahoma.com

Central Oklahoma Master Conservancy District

12500 East Alameda

Norman, OK 73071

Internet: N/A

Phone: (405)

Fax: (405)

Oklahoma Conservation Commission

2800 N. Lincoln, Suite 160
Oklahoma City, Oklahoma 73105

Internet: www.conservation.ok.gov

Phone: (405) 521-2384

Fax: (405) 521-6686

Water Research Institute

003 Life Sciences East

Stillwater, OK 74078

Internet: http://okwaterplan.info

Phone: (405) 744-9994

Fax: (405) 744-7074

United States Army Corps of Engineers

1645 S 101 E Ave
Tulsa, OK 74128-4609

Internet: www.swt.usace.army.mil

Phone: (918) 669-7366

Fax: (918) 669-7368

Friends of Lake Thunderbird

Stephen Foley - President

Phone: (405) 641-4185

Phone: (405) 360-3572
Fax: (405) 366-8150

| DATE |  | SPECIES |  | SIZE |  | NUMBER |  | WEIGHT LBS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1/27/1965 |  | Largemouth bass |  | N/A |  | 19,860 |  | N/A |
| 1/28/1965 |  | Largemouth bass |  | N/A |  | 35,880 |  | N/A |
| 7/12/1965 |  | Largemouth bass |  | Fry |  | 250,000 |  | N/A |
| 7/12/1965 |  | Flathead catfish |  | Fry |  | 2,475 |  | 17.83 |
| 1966 |  | Blue catfish |  | N/A |  | N/A |  | N/A |
| 1/31/1966 |  | Channel catfish |  | N/A |  | 48,750 |  | 3.5 |
| 3/28/1966 |  | Walleye |  | Fry |  | 500,000 |  | N/A |
| 3/30/1966 |  | Threadfin shad |  | Adult |  | 2,500 |  | N/A |
| 3/31/1966 |  | Largemouth bass |  | N/A |  | 80,217 |  | N/A |
| 3/1/67 |  | Walleye |  | Fry |  | 500,000 |  | N/A |
| 3/2/1968 |  | Walleye |  | Adult |  | 6 |  | 12 |
| 3/25/1968 |  | Walleye |  | Fry |  | 500,000 |  | N/A |
| 4/10/1969 |  | Walleye |  | Fry |  | 250,000 |  | N/A |
| 10/24/1973 |  | Florida largemouth bass |  | Fingerlings |  | 1,150 |  | 95.83 |
| 3/22/1974 |  | Walleye |  | Fry |  | 1,092,042 |  | N/A |
| 3/25/1974 |  | Walleye |  | Fry |  | 1,320,769 |  | N/A |
| 4/1/1974 |  | Walleye |  | Fry |  | 562,224 |  | N/A |
| 7/9/1974 |  | Florida largemouth bass |  | 3 - 3.5 |  | 5,400 |  | 70.0 |
| 7/26/1974 |  | Largemouth bass |  | 3 - 5.0 |  | 5,000 |  | 79.0 |
| 3/25/1975 |  | Walleye |  | Fry |  | 111,200 |  | N/A |
| 3/28/1975 |  | Walleye |  | Fry |  | 337,000 |  | N/A |
| 3/31/1975 |  | Walleye |  | Fry |  | 1,900,000 |  | N/A |
| 4/4/1975 |  | Walleye |  | Fry |  | 477,500 |  | N/A |
| 4/18/1975 |  | Walleye |  | Fry |  | 278,500 |  | N/A |
| 7/3/1975 |  | Largemouth bass |  | Fingerling |  | 50,000 |  | 50 |
| 8/11/1975 |  | Florida largemouth bass |  | Adv. Fry |  | 1,054 |  | 2.5 |
| 9/9/1975 |  | Florida largemouth bass |  | N/A |  | 5,909 |  | 6.3 |
| 3/21/1976 |  | Walleye |  | Fry |  | 260,300 |  | N/A |
| 3/27/1976 |  | Walleye |  | Fry |  | 146,000 |  | N/A |
| 3/29/1976 |  | Walleye |  | Fry |  | 300,000 |  | N/A |
| 3/30/1976 |  | Walleye |  | Fry |  | 99,000 |  | N/A |
| 4/1/1976 |  | Walleye |  | Fry |  | 195,000 |  | N/A |
| 9/30/1983 |  | Channel catfish |  | 3.0 |  | 30,475 |  | 244.0 |
| 10/5/1983 |  | Channel catfish |  | 3.0 |  | 33,480 |  | 273.37 |
| 1985 |  | Saugeye |  | Fry |  | 98,000 |  | N/A |
| 1985 |  | Threadfin shad |  | Adult |  | 13,700 |  | N/A |
| 3/31/1986 |  | Saugeye |  | Fry |  | 94,080 |  | N/A |
| 4/25/1986 |  | Saugeye |  | 1 |  | 111,000 |  | 37.0 |
| 1986 |  | Threadfin shad |  | Adult |  | 15,280 |  | N/A |
| 5/5/1987 |  | Saugeye |  | 1.5 |  | 23,500 |  | 23.14 |
| 5/8/1987 |  | Saugeye |  | 1.25 - 1.75 |  | 58,150 |  | 51.81 |
| 1987 |  | Threadfin shad |  | Adult |  | 2,000 |  | N/A |
| 5/5/1988 |  | Saugeye |  | 1.25 |  | 33,400 |  | 22.3 |
| 5/6/1988 |  | Saugeye |  | 1.25 |  | 96,000 |  | 64.0 |
| 5/10/1988 |  | Saugeye |  | 1.25 |  | 42,000 |  | 28.0 |
| 1988 |  | Threadfin shad |  | Adult |  | 3,000 |  | N/A |
| 4/24/1989 |  | Saugeye |  | 1.5 |  | 80,000 |  | 55.8 |
| 4/27/1989 |  | Saugeye |  | 1.25 |  | 40,500 |  | 30.0 |
| 4/28/1989 |  | Saugeye |  | 1.5 |  | 45,000 |  | 50 |
| DATE |  | SPECIES |  | SIZE |  | NUMBER |  | WEIGHT LBS |
| 4/2/1990 |  | Saugeye |  | Fry |  | 125,000 |  | N/A |
| 1989 |  | Threadfin shad |  | Adult |  | 6,700 |  | N/A |
| 5/21/1990 |  | Saugeye |  | 1.5 |  | 100,176 |  | 131.82 |
| 5/24/1990 |  | Saugeye |  | 1.25 - 1.5 |  | 126,880 |  | 136.75 |
| 7/13/1990 |  | Flathead catfish |  | 1.0 |  | 10,250 |  | 1.5 |
| 9/11/1990 |  | Florida largemouth bass |  | 5.0 - 10.0 |  | 3,769 |  | N/A |
| 1990 |  | Threadfin shad |  | Adult |  | 10,000 |  | N/A |
| 5/2/1991 |  | Saugeye |  | 1.25 |  | 74,350 |  | 62 |
| 7/26/1991 |  | Florida largemouth bass |  | 3.0 - 6.0 |  | 2,022 |  | 48 |
| 5/14/1991 |  | Saugeye |  | 2.0 |  | 20,500 |  | 34.9 |
| 4/28/1992 |  | Saugeye |  | 1.125 |  | 63,000 |  | 42 |
| 5/26/1992 |  | Saugeye |  | 1.75 |  | 49,075 |  | 75.5 |
| 5/27/1992 |  | Saugeye |  | 1.5 -1.75 |  | 70,625 |  | 97.5 |
| 9/28/1992 |  | Florida largemouth bass |  | 3.0 - 5.0 |  | 930 |  | 27.4 |
| 5/12/1993 |  | Florida largemouth bass |  | Fry |  | 10,000 |  | N/A |
| 5/17/1993 |  | Saugeye |  | 1.75 |  | 24,623 |  | 40.8 |
| 5/18/1993 |  | Saugeye |  | 1.75 - 2.0 |  | 30,900 |  | 60 |
| 6/3/1993 |  | Saugeye |  | 1.5 |  | 54,000 |  | 65 |
| 6/16/1993 |  | Florida largemouth bass |  | Fry |  | 700 |  | N/A |
| 9/21/1993 |  | Florida largemouth bass |  | 3.0 |  | 1,782 |  | 21.7 |
| 9/21/1993 |  | Florida largemouth bass |  | 9.0 |  | 111 |  | 35.8 |
| 5/9/1994 |  | Saugeye |  | 1.6 - 1.75 |  | 52,570 |  | 87 |
| 5/11/1994 |  | Saugeye |  | 1.5 - 1.6 |  | 36,707 |  | 49 |
| 9/19/1994 |  | Florida largemouth bass |  | 3.0 - 5.0 |  | 292 |  | N/A |
| 9/19/1994 |  | Florida largemouth bass |  | 6.0 - 8.0 |  | 180 |  | N/A |
| 6/14/1995 |  | Saugeye |  | 1.5 |  | 120,000 |  | 122 |
| 6/13/1995 |  | Saugeye |  | 1.5 - 2.0 |  | 27,700 |  | N/A |
| 5/29/1996 |  | Saugeye |  | 1.5 |  | 70,034 |  | 87.5 |
| 6/5/1996 |  | Saugeye |  | 1.6 |  | 49,000 |  | 59 |
| 7/10/1997 |  | Florida largemouth bass |  | 3.0 - 6.0 |  | 6,560 |  | N/A |
| 5/15/1998 |  | Saugeye |  | 2.0 |  | 87,600 |  | 146 |
| 5/26/1998 |  | Saugeye |  | 1.75 |  | 34,710 |  | 39 |
| 11/4/1998 |  | Florida largemouth bass |  | 3.0 - 5.0 |  | 998 |  | 37.5 |
| 11/4/1998 |  | Florida largemouth bass |  | 6.0 - 10.0 |  | 411 |  | 34.5 |
| 5/10/2000 |  | Saugeye |  | 2.0 |  | 27,000 |  | 45 |
| 5/31/2000 |  | Saugeye |  | 1.5 |  | 56,525 |  | 59.5 |
| 6/1/2000 |  | Saugeye |  | 1.5 |  | 37,660 |  | 37.6 |
| 11/21/2000 |  | Florida Largemouth bass |  | 6.0 - 7.0 |  | 2,048 |  | 128 |
| 1/21/2000 |  | Florida Largemouth bass |  | 4.0 - 6.0 |  | 260 |  | N/A |
| 4/29/2002 |  | Saugeye |  | 1.5 |  | 51,500 |  | 51.5 |
| 5/6/2002 |  | Saugeye |  | 1.5 |  | 70,500 |  | 70.5 |
| 6/20/2002 |  | Florida largemouth bass |  | 3.0 |  | 18,000 |  | 120 |
| 5/5/2003 |  | Saugeye |  | 1.5 |  | 28,750 |  | 50 |
| 5/5/2003 |  | Saugeye |  | 1.5 |  | 33,280 |  | 52 |
| 5/6/2003 |  | Saugeye |  | 1.5 |  | 44,520 |  | 85 |
| 5/13/2003 |  | Saugeye |  | 1.5 |  | 20,000 |  | 22 |
| 10/16/2003 |  | Florida largemouth bass |  | 5.0 |  | 1,460 |  | N/A |
| 5/2/2005 |  | Saugeye |  | 1.5 |  | 64,200 |  | 85 |
| 5/3/2005 |  | Saugeye |  | 1.5 |  | 56,550 |  | 76 |
| DATE |  | SPECIES |  | SIZE |  | NUMBER |  | WEIGHT LBS |
| 5/18/2005 |  | Saugeye |  | 2.0 |  | 20,100 |  | 33.5 |
| 5/8/2006 |  | Saugeye |  | 1.75 |  | 96,900 |  | 96 |
| 5/9/2006 |  | Saugeye |  | 1.75 |  | 24,000 |  | 48 |
| 5/8/2007 |  | Saugeye |  | 1.5 |  | 51,900 |  | 79.8 |
| 5/9/2007 |  | Saugeye |  | 1.5 |  | 45,500 |  | 65 |
| 5/5/2008 |  | Saugeye |  | 1.5 |  | 89,100 |  | 78 |
| 5/6/2008 |  | Saugeye |  | 1.5 |  | 33,760 |  | 32 |
| Total |  |  |  |  |  | 12,302,969 |  |  |

| Table 2. Largemouth bass total catch rate, catch rate by size group and mean relative weight (Wr) from Lake Thunderbird |  |  |
| --- | --- | --- |
|  |  | Total C/f |  |  |  | C/f ≥ 356 mm |  |  |  |  |
| Year |  | (≥ 40 is preferred) |  | (C/f) ≤ 200mm |  | (≥ 10 is preferred) |  | Effort (hrs) |  | (Wr) |
| 1983 |  | 12.12 |  | 1.36 |  | 6.20 |  | 32.25 |  | 103 |
| 1984 |  | N/A |  | N/A |  | N/A |  | N/A |  | N/A |
| 1985 |  | 21.05 |  | 1.89 |  | 13.26 |  | 4.75 |  | 105 |
| 1986 |  | 24.43 |  | 2.43 |  | 9.43 |  | 7.00 |  | 93 |
| 1987 |  | 15.69 |  | 2.15 |  | 8.61 |  | 6.50 |  | 98 |
| 1988 |  | 22.69 |  | 7.23 |  | 6.00 |  | 13.00 |  | 95 |
| 1989 |  | 26.60 |  | 5.76 |  | 8.93 |  | 10.75 |  | 93 |
| 1990 |  | 56.33 |  | 17.33 |  | 6.66 |  | 3.00 |  | 94 |
| 1991 |  | 54.25 |  | 35.00 |  | 7.50 |  | 4.00 |  | 96 |
| 1992 |  | 35.16 |  | 10.16 |  | 10.16 |  | 6.00 |  | 97 |
| 1993 |  | 31.44 |  | 2.66 |  | 11.55 |  | 9.00 |  | 98 |
| 1994 |  | 28.91 |  | 2.40 |  | 14.85 |  | 8.75 |  | 99 |
| 1995 |  | 19.78 |  | 1.05 |  | 11.78 |  | 4.75 |  | 101 |
| 1996 |  | 8.16 |  | 0.08 |  | 5.00 |  | 6.00 |  | 95 |
| 1997 |  | 15.09 |  | 1.161 |  | 9.16 |  | 7.75 |  | 103 |
| 1998 |  | N/A |  | N/A |  | N/A |  | N/A |  | N/A |
| 1999 |  | N/A |  | N/A |  | N/A |  | N/A |  | N/A |
| 2000 |  | N/A |  | N/A |  | N/A |  | N/A |  | N/A |
| 2001 |  | N/A |  | N/A |  | N/A |  | N/A |  | N/A |
| 2002 |  | 36.18 |  | 14.54 |  | 10.18 |  | 5.50 |  | 100 |
| 2003 |  | 22.83 |  | 4.50 |  | 7.33 |  | 6.00 |  | 97 |
| 2004 |  | 12.42 |  | 1.68 |  | 6.74 |  | 4.75 |  | 112 |
| 2005 |  | 41.71 |  | 10.28 |  | 17.14 |  | 5.25 |  | 93 |
| 2006 |  | 41.55 |  | 4.22 |  | 20.00 |  | 4.50 |  | 103 |
| 2007 |  | 8.32 |  | 0.80 |  | 5.29 |  | 5.25 |  | 104 |
| 2008 |  | 16.22 |  | 3.33 |  | 9.33 |  | 4.50 |  | 98 |
| Gear = Spring electrofishing |  |  |  |  |  |  |  |  |

| Table 3. White crappie total catch rate, catch rate by size group and mean relative weight (Wr) from Lake Thunderbird |
| --- |
| Year |  | (C/f) |  | (C/f) ≥ 250 mm |  | Effort |  | (Wr) |
| 1983 |  | 138.20 |  | 0.22 |  | 1147 |  | 91 |
| 1984 |  | 88.80 |  | 1.49 |  | 337 |  | 85 |
| 1985 |  | 135.48 |  | 1.87 |  | 549 |  | 84 |
| 1986 |  | 87.62 |  | 2.42 |  | 375 |  | 85 |
| 1987 |  | 54.62 |  | 2.11 |  | 490 |  | 85 |
| 1988 |  | 65.38 |  | 2.54 |  | 377 |  | 86 |
| 1989 |  | 29.59 |  | 0.74 |  | 774 |  | 86 |
| 1990 |  | 34.42 |  | 2.71 |  | 583 |  | 85 |
| 1991 |  | 50.88 |  | 1.70 |  | 407 |  | 83 |
| 1992 |  | 38.64 |  | 0.84 |  | 374 |  | 86 |
| 1993 |  | 31.75 |  | 2.14 |  | 572 |  | 87 |
| 1994 |  | 40.01 |  | 1.51 |  | 552 |  | 85 |
| 1995 |  | 24.60 |  | 0.86 |  | 551 |  | 84 |
| 1996 |  | 13.03 |  | 1.75 |  | 578 |  | 91 |
| 1997 |  | 9.14 |  | 1.90 |  | 569 |  | 90 |
| 1998 |  | 23.11 |  | 1.18 |  | 590 |  | 89 |
| 1999 |  | 50.16 |  | 1.06 |  | 542 |  | 86 |
| 2000 |  | N/A |  | N/A |  | N/A |  | N/A |
| 2001 |  | 19.54 |  | 3.82 |  | 560 |  | 86 |
| 2002 |  | 13.70 |  | 1.78 |  | 564 |  | 83 |
| 2003 |  | 18.60 |  | 1.90 |  | 542 |  | 90 |
| 2004 |  | 21.91 |  | 4.03 |  | 564 |  | 85 |
| 2005 |  | 62.40 |  | 4.56 |  | 510 |  | 81 |
| Gear = Fall trapnetting |  |  |  |  |  |  |

| Table 4. Saugeye total catch rate, catch rate by size group and mean relative weight (Wr) from Lake Thunderbird |  |
| --- | --- |
| Year |  | (C/f) |  | (C/f) ≥ 457 mm ( ≥ 10 preferred) |  | Effort |  | (Wr) |
| 1985* |  | N/A |  | 0.00 |  | N/A |  | N/A |
| 1986 |  | N/A |  | N/A |  | N/A |  | N/A |
| 1987 |  | 15.56 |  | 5.33 |  | 4.50 |  | 100 |
| 1988 |  | N/A |  | N/A |  | N/A |  | N/A |
| 1989 |  | N/A |  | N/A |  | N/A |  | N/A |
| 1990 |  | N/A |  | N/A |  | N/A |  | N/A |
| 1991 |  | N/A |  | N/A |  | N/A |  | N/A |
| 1992 |  | 8.00 |  | 7.20 |  | 1.25 |  | 94 |
| 1993 |  | 8.21 |  | 7.16 |  | 4.75 |  | 106 |
| 1994 |  | 7.69 |  | 6.31 |  | 6.50 |  | 99 |
| 1995 |  | N/A |  | N/A |  | N/A |  | N/A |
| 1996 |  | 58.50 |  | 27.50 |  | 6.75 |  | N/A |
| 1997 |  | 25.88 |  | 20.70 |  | 4.25 |  | 105 |
| 1998 |  | 24.89 |  | 20.67 |  | 4.50 |  | 100 |
| 1999 |  | 46.00 |  | 16.40 |  | 2.50 |  | 89 |
| 2000 |  | N/A |  | N/A |  | N/A |  | N/A |
| 2001 |  | 13.91 |  | 11.24 |  | 5.25 |  | 94 |
| 2002 |  | 26.91 |  | 20.55 |  | 5.50 |  | 95 |
| 2003 |  | 14.67 |  | 13.60 |  | 3.75 |  | 108 |
| 2004 |  | N/A |  | N/A |  | N/A |  | N/A |
| 2005 |  | 22.00 |  | 14.00 |  | 4.50 |  | 93 |
| 2006 |  | 24.00 |  | 8.86 |  | 3.50 |  | 100 |
| 2007 |  | N/A |  | N/A |  | N/A |  | N/A |
| Gear = Fall day electrofishing |  |  |  |  |  |  |

| Table 5. Flathead catfish catch rate and mean relative weight (Wr) from Lake Thunderbird |
| --- |
| Year |  | (C/f) |  | Effort |  | (Wr) |  |
| 1983 |  | N/A |  | N/A |  | N/A |  |
| 1984 |  | N/A |  | N/A |  | N/A |  |
| 1985 |  | N/A |  | N/A |  | N/A |  |
| 1986 |  | N/A |  | N/A |  | N/A |  |
| 1987 |  | N/A |  | N/A |  | N/A |  |
| 1988 |  | N/A |  | N/A |  | N/A |  |
| 1989 |  | N/A |  | N/A |  | N/A |  |
| 1990 |  | N/A |  | N/A |  | N/A |  |
| 1991 |  | 15 |  | 2 |  | 112 |  |
| 1992 |  | 43.529 |  | 2 |  | 109 |  |
| 1993 |  | 14.762 |  | 2.1 |  | 113 |  |
| 1994 |  | 67.619 |  | 1.05 |  | 119 |  |
| 1995 |  | 33 |  | 1 |  | 124 |  |
| 1996 |  | 24 |  | 1 |  | 109 |  |
| 1997 |  | N/A |  | N/A |  | N/A |  |
| 1998 |  | N/A |  | N/A |  | N/A |  |
| 1999 |  | N/A |  | N/A |  | N/A |  |
| 2000 |  | N/A |  | N/A |  | N/A |  |
| 2001 |  | N/A |  | N/A |  | N/A |  |
| 2002 |  | 56 |  | 1 |  | 86 |  |
| 2003 |  | N/A |  | N/A |  | N/A |  |
| 2004 |  | N/A |  | N/A |  | N/A |  |
| 2005 |  | N/A |  | N/A |  | N/A |  |
| 2006 |  | N/A |  | N/A |  | N/A |  |
| 2007 |  | N/A |  | N/A |  | N/A |  |
| Gear = Roving electrofishing |  |  |  |  |  |

| Year |  | Num / Day |  | % Success |  | Hrs / 5-lb |
| --- | --- | --- | --- | --- | --- | --- |
| 1994 |  | 0.85 |  | 51.35 |  | N/A |
| 1995 |  | 0.99 |  | 64.96 |  | 164 |
| 1996 |  | 0.67 |  | 35.30 |  | 190 |
| 1997 |  | 0.73 |  | 37.32 |  | 88 |
| 1998 |  | 0.95 |  | 42.77 |  | 100 |
| 1999 |  | 0.91 |  | 43.09 |  | 54 |
| 2000 |  | 0.91 |  | 40.96 |  | 72 |
| 2001 |  | 0.79 |  | 35.55 |  | 127 |
| 2002 |  | 0.69 |  | 35.08 |  | 206 |
| 2003 |  | 1.03 |  | 42.75 |  | 199 |
| 2004 |  | 1.88 |  | 52.78 |  | 175 |
| 2005 |  | 1.58 |  | 37.88 |  | 153 |
| 2006 |  | 3.35 |  | 61.18 |  | 102 |
| 2007 |  | 1.88 |  | 39.91 |  | 53 |

| Table 7. Harvest and angler pressure values for largemouth bass at Lake Thunderbird from 1985 to 1995 |
| --- |
| Year |  | Pressure (Hrs / A) |  | C/f (N / hr) |  | Total harvest (Fish / A) |
| 1985 |  | 18.81 |  | 0.04 |  | 0.68 |
| 1986 |  | 23.68 |  | 0.06 |  | 0.66 |
| 1987 |  | 13.94 |  | 0.03 |  | 0.30 |
| 1988 |  | 18.13 |  | 0.05 |  | 0.14 |
| 1989 |  | 20.55 |  | 0.04 |  | 0.22 |
| 1990 |  | 22.28 |  | 0.08 |  | 0.32 |
| 1991 |  | 22.00 |  | 0.09 |  | 0.15 |
| 1992 |  | 21.52 |  | 0.09 |  | 0.27 |
| 1993 |  | 14.83 |  | 0.12 |  | 0.24 |
| 1994 |  | 15.49 |  | 0.13 |  | 0.22 |
| 1995 |  | 19.03 |  | 0.12 |  | 0.35 |

| Table 8. Harvest and angler pressure values for crappie at Lake Thunderbird from 1985 to 1995 |
| --- |
| Year |  | Pressure (Hrs / A) |  | C/f (N / hr) |  | Total harvest (Fish / A) |
| 1985 |  | 18.81 |  | 0.21 |  | 0.92 |
| 1986 |  | 23.69 |  | 0.50 |  | 4.72 |
| 1987 |  | 14.14 |  | 0.58 |  | 3.10 |
| 1988 |  | 18.13 |  | 0.33 |  | 2.00 |
| 1989 |  | 20.55 |  | 0.57 |  | 4.12 |
| 1990 |  | 22.28 |  | 0.28 |  | 4.31 |
| 1991 |  | 22.00 |  | 0.44 |  | 4.60 |
| 1992 |  | 21.52 |  | 0.33 |  | 2.85 |
| 1993 |  | 14.83 |  | 0.62 |  | 2.90 |
| 1994 |  | 15.49 |  | 1.08 |  | 7.52 |
| 1995 |  | 19.03 |  | 0.71 |  | 5.11 |

| Table 9. Harvest and angler pressure for saugeye at Lake Thunderbird from 1985 to 1995 |
| --- |
| Year |  | Pressure (Hrs / A) |  | C/f (N / hr) |  | Total harvest (Fish / A) |
| 1985 |  | N/A |  | N/A |  | N/A |
| 1986 |  | 23.68 |  | 0.006 |  | 0.11 |
| 1987 |  | 13.94 |  | 0.007 |  | 0.10 |
| 1988 |  | 18.13 |  | 0.016 |  | 0.17 |
| 1989 |  | 20.55 |  | 0.009 |  | 0.14 |
| 1990 |  | 22.28 |  | 0.003 |  | 0.06 |
| 1991 |  | 20.38 |  | 0.017 |  | 0.14 |
| 1992 |  | 21.52 |  | 0.012 |  | 0.19 |
| 1993 |  | 14.83 |  | 0.022 |  | 0.09 |
| 1994 |  | 15.49 |  | 0.033 |  | 0.08 |
| 1995 |  | 19.03 |  | 0.033 |  | 0.16 |
| N/A = First year of saugeye introductions |  |  |  |  |

| Table 10. Harvest and angler pressure values for blue and channel catfish at Lake Thunderbird from 1985 to 1995 |
| --- |
| Year |  | Pressure (Hrs / A) |  | C/f (N / hr) |  | Total harvest (Fish / A) |
| 1985 |  | 18.81 |  | 0.108 |  | 1.17 |
| 1986 |  | 23.68 |  | 0.129 |  | 1.50 |
| 1987* |  | 13.94 |  | 0.004 |  | 0.04 |
| 1988 |  | 18.13 |  | 0.090 |  | 0.82 |
| 1989 |  | 20.55 |  | 0.046 |  | 0.67 |
| 1990 |  | 22.28 |  | 0.085 |  | 1.82 |
| 1991 |  | 20.38 |  | 0.074 |  | 1.39 |
| 1992 |  | 21.52 |  | 0.062 |  | 0.87 |
| 1993 |  | 14.83 |  | 0.038 |  | 0.57 |
| 1994 |  | 15.49 |  | 0.058 |  | 0.84 |
| 1995 |  | 19.03 |  | 0.044 |  | 0.61 |
| * - Channel catfish only |  |  |  |  |

Table 11.  Marked “Fishing Areas” and descriptions

| ID # | Habitat Type | Area Name | Marked | Bank Access | Date Installed | Depth (ft) | Latitude | Longitude |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Brush Row | South Dam Cove | No | Yes | 2002 | 6 to 8 | 35° 12' 59" | 97° 13' 31" |
| 2 | Brush Pile | Five Finger Cove | Yes | No | 2006 | 12 to 15 | 35° 14' 27" | 97° 13' 18" |
| 3 | Brush Row | Willow Branch Cove | Yes | No | 2006 | 10 to 15 | 35° 15' 47" | 97° 14' 04" |
| 4 | Brush Pile | New House Cove | Yes | No | 2005 | 8 to 12 | 35° 13' 29" | 97° 16' 18" |
| 5 | Brush Pile | Snake Pit Cove | Yes | No | 2005 | 12 to 15 | 35° 13' 02" | 97° 16' 34" |
| 6 | Brush Row | Clear Bay East | Yes | No | 2005 | 12 to15 | 35° 12' 06" | 97° 15' 23" |
| 7 | Brush Pile | Sullivan's Cove | Yes | No | 2005 | 8 to 10 | 35° 13' 42" | 97° 17' 18" |
| 8 | Brush Pile | Hog Creek (East) | Yes | No | 2006 | 8 to 12 | 35° 14' 51" | 97° 13' 44" |
| 9 | Brush Pile | Denver Corner Ramp | No | Yes | 2005 | 5 to 10 | 35° 13' 35" | 97° 16' 51" |
| 10 | Brush Pile | Indian Point | No | No | 2004 | 8 to 12 | 35° 15' 03" | 97° 14' 34" |
| 11 | Brush Pile | Fisherman's Pt. Pier | No | Yes | 2005 | 5 to 8 | 35° 13' 46" | 97° 14' 46" |
| 12 | Gravel Piles | Clear Bay West | No | No | 2007 | 5 to 20 | 35° 12' 45" | 97° 15' 25" |
| 13 | Gravel Piles | Little Axe Campground | No | Yes | 2006 | 5 to 10 | 35° 13' 59" | 97° 13' 24" |

Figure 1.  ODWC “Fish attractor” locations

Table with GPS coordinates for “Fishing Area” sites

# Text boxes

Table 1.  ODWC fish stocking records for Lake Thunderbird (impoundment to present)

Table 1.  ODWC fish stocking records for Lake Thunderbird (impoundment to present)

Table 1.  ODWC fish stocking records for Lake Thunderbird (impoundment to present)

Table 6.  Bass tournament averages at Lake Thunderbird from 1994 to 2007